## Slide 1
Team Name : ICE
Problem Statement : Predictive Maintenance and OEE Command Center
Team Leader Name : Amogh Kotha Nagaraj
Team Size : 1
FactoryPulse — IT/OT converged predictive maintenance with a local Granite agent

## Slide 2
Problem Brief: breakdowns hide in the OT/IT gap
Discrete manufacturing (machining, pressing, conveying, pumping) · Industry 4.0 IT/OT convergence
1
Real business problem
Sensors show vibration and temperature drifting 24-48 h before a breakdown, but that data lives in OT historians.
Production schedule, maintenance history, parts and cost live in ERP/CMMS. Nobody sees both at once.
Result: failures are discovered when the machine stops, and OEE loss is explained weeks later.
2
Target users
Reliability engineer / maintenance planner: who to inspect today, and why.
Shift supervisor: what the line will deliver this shift and which asset is at risk.
Plant manager: OEE by line and the cost of unplanned downtime.
3
Pain today → with FactoryPulse
Found at breakdown → predicted ~20 h ahead, with drivers.
Manual work order after the fact → P1 WO auto-created with evidence.
Root cause = days across systems → grounded answer in seconds.
OEE reported monthly → live by asset/line, tied to the cause.
4
Why now / domain context
IT/OT convergence is the core of Industry 4.0 programmes; the data already exists, it is just siloed.
Small local LLMs (Granite 4.0 1B) now run on a plant PC: no cloud round-trip for sensitive OT data.
Snowflake Dynamic Tables, Tasks and Cortex Analyst give the same design a governed cloud twin.

## Slide 3
Architecture: one pipeline from sensor stream to work order
Local MVP: SQLite · scikit-learn · Streamlit · Granite 4.0 1B GGUF | Snowflake twin: Dynamic Tables · Model Registry · Task · Cortex Analyst
DATA SOURCES
CONVERGED FEATURES
PREDICT & ACT
EXPERIENCE
OT · sensor stream
vibration, temp, RPM, status
5-min samples · structured
IT · ERP production orders
planned/run min, counts, scrap
per shift · structured
IT · CMMS work orders
type, parts, cost, technician
free-text findings · unstructured
Hourly feature table
rolling stats, trends, baselines
+ hours since maintenance (IT)
OEE daily
Availability × Perf. × Quality
Snowflake: Dynamic Table
Evidence pack builder
sensor deltas, drivers, WO history
production context, for grounding
Failure model (GBM)
P(failure in 24 h) + top drivers
holdout-tested · Model Registry
Alert engine + rule limits
risk ≥ 0.7 CRITICAL · ≥ 0.4 WARNING
dedupe, auto-resolve, safety net
Work-order automation
P1 predictive WO with evidence
one WO per asset · 15-min Task
Streamlit command center
overview, triage, asset explorer,
work orders, system health
Ask in natural language
verified queries → guarded SQL
read-only, auto-LIMIT, retry
Root cause · Granite 1B
grounded on the evidence pack
rule-based fallback if LLM is down
CoCo CLI skills used, and how they connect
Synthetic data generation: referentially consistent OT + ERP + CMMS sets, no production data
Data pipeline creation: hourly features & OEE as Dynamic Tables; scheduled scoring Task
Semantic model authoring: Cortex Analyst YAML with verified queries (same tier as the app)
Streamlit app generation: command center scaffolded and iterated in CoCo
Automation + guardrails: unattended runs, read-only SQL guard, alert dedupe, LLM fallback
Reusable skill: coco/skills/factorypulse-pipeline: build, run, validate, deploy

## Slide 4
Impact: measurable now, scalable, extensible later
Figures from the generated plant (8 assets, 30 days, 17 unplanned failures, forward-looking holdout on the last 30 % of the timeline)
0.98
ROC-AUC on holdout
91%
of failure hours flagged in the 24 h window (recall)
~20 h
average warning lead time before breakdown
83 h
unplanned downtime in 30 days (~5 h per event)
< 1 min
from CRITICAL alert to P1 work order (was hours)
1
Measurable outcomes
Precision 87% / recall 91%: few false alarms, most failures caught a shift ahead.
Every CRITICAL alert carries its drivers and opens a work order with evidence, cutting triage from hours to seconds.
Root-cause narrative in ~10 s and data questions in ~3 s on a CPU-only plant PC, grounded and audited.
If 9 of 10 failures become planned interventions, most of the 83 h/month of unplanned downtime turns into shorter, scheduled work.
2
Scalability potential
Snowflake twin: Dynamic Tables refresh incrementally, a Task scores every 15 min, the model sits in the Model Registry.
Adding assets, lines or plants adds rows, not code: features, OEE and alerts are all per-asset.
Cortex Analyst semantic model exposes the same verified queries in Snowsight agents and the Slackbot.
Sensitive OT data can stay on site with the local Granite model; cloud handles scale and governance.
3
Beyond the demo
Replace synthetic feeds with Snowpipe Streaming / Kafka for historians and ERP connectors for SAP.
MCP connectors to the CMMS (SAP PM, Maximo) and Slack so the agent creates and routes real work orders.
Feedback loop: closed work orders with technician verdicts retrain the model and refine failure modes.
Survival model for time-to-failure, spare-parts forecasting, and a triage → RCA → planner multi-agent flow.

## Slide 5
Additional Slide
CoCo across the lifecycle, guardrails, and the 3-minute demo
1
Planning
coco/PLAN.md: problem framing, ontology, workflow, design decisions, validation plan drafted before the build
2
Development
pipeline, model, Streamlit app, Snowflake DDL / Dynamic Tables / semantic model built and iterated in CoCo
3
Execution
run_pipeline.py end-to-end; simulate_stream.py near-real-time ticks; scheduled Snowflake Task for unattended scoring
4
Testing
20 pytest checks: data integrity, OEE math, model floor, alert guardrails, SQL guard, LLM-free fallback
G
Guardrails and graceful fallback
Natural-language path can never write: single SELECT only, forbidden keywords blocked, auto-LIMIT, read-only connection.
Verified queries answer common questions deterministically before the LLM is involved.
Alerts de-duplicated per asset/type; only CRITICAL opens a work order; one open WO per asset; auto-resolve on recovery.
Hard sensor limits (7.1 mm/s, 85 °C) alert even if the model is missing; LLM outage falls back to rule-based narrative.
The LLM only sees the evidence pack, which is displayed next to every answer for audit.
D
Demo flow
Overview opens with CNC-002 and PMP-001 at CRITICAL, two auto-created P1 work orders, plant OEE by line.
Alert triage: acknowledge, open the 72 h sensor view, ask Granite for the root cause (bearing wear signature).
Investigate: "Which asset had the most unplanned downtime?" (verified) and a free-form question (text-to-SQL).
Second terminal: simulate_stream.py --degrade CNC-003 raises a live alert and work order within a minute.
Repo: github.com/Amogh892/factorypulse-oee-command-center